## Slide 1
New Circle Road Improvement Project
Intersection Concepts under Consideration
Fayette County
KYTC Item No. 7-438

## Slide 2
Introduction
This brief presentation will explain some of the intersection concepts the KY Transportation Cabinet project team is considering to improve safety and traffic operations for the New Circle Road Improvement Project

## Slide 3
Restricted Crossing U-Turn (RCUT) Intersection
An RCUT, sometimes referred to as a J-Turn, allows normal turning movements from the major route but allows only right turns from the minor approaches. Vehicles wishing to turn left must make a right turn and then a U-turn.
What is an RCUT?
Benefits
Traffic: The traffic signal at the main intersection operates with just two signal phases.
Safety: All crashes are reduced by about 35% compared to a standard signalized intersection

## Slide 4
Restricted Crossing U-Turn (RCUT) Intersection
U-turn
Traffic on Woodhill & Life Ln. can only turn right
Traffic on New Circle can only access Woodhill & Life Ln. via right turn
Pedestrians cross New Circle via tunnel system

## Slide 5
Bowtie Roundabout Intersection
A Bowtie roundabout is an intersection where left-turn movements are completed at adjacent roundabouts on the side street.
What is a Bowtie Roundabout?
Benefits
Safety: Reduces the number of conflict points, promotes lower speeds.
Traffic: There are no left turns at the main intersection, reducing stops and delay. Fewer traffic signal phases means less stopping time at the main intersection.
Left-Turn

## Slide 6
Bowtie Roundabout
Liberty Rd.
Christian Rd.
Wilderness Rd.
Creative Dr.
Traffic on New Circle can only turn right
Traffic on Liberty can turn right or continue through
U-turn
U-turn
Pedestrians can cross New Circle via tunnel

## Slide 7
Grade Separation
Removing an intersection by separating two roadways with an overpass.
What is Grade Separation?
Safety: Removes conflict points at the intersection.
Traffic: Traffic does not stop (on both the main route and side street).
Woodhill Dr.
Life Ln.
No access to Woodhill or Life Ln. from New Circle
Pedestrians cross New Circle under the overpass
Benefits

## Slide 8
Intersection Options Under Consideration
Intersection | Conventional Widening | RCUT | Bowtie | Grade Separation
Woodhill Drive | X | X |  | X
Palumbo Drive | X | X |  | 
Young Drive | X | X |  | 
Liberty Road | X |  | X | X